## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – 26126
Problem Statement Title – Vision Based Autonomous Navigation for Unmanned Ground Vehicle for Outdoor environment
Theme – Smart Automation
PS Category – Software
Team ID – <Team ID>
Team Name – The Vikings
SIH 2025 GRAND FINALE FINALIST
Team The Vikings — returning to Smart India Hackathon 2026

## Slide 2: IDEA TITLE
THE VIKINGS
SIH 2025 FINALIST
DRISHTI-UGV — a vision-first autonomy module that drives an outdoor UGV from Point A to Point B with no GPS
THE PROBLEM
OUR SOLUTION
01
GPS is denied or unreliable
Tree cover, terrain masking and jamming remove any trusted fix.
02
Open ground is not safe ground
A ditch, mud patch or slope still reads as free space.
03
Obstacles appear after planning
People, animals and vehicles cross the path mid-mission.
04
Vision degrades without warning
Glare, shadow and low light silently break a camera-only stack.
A
Visual SLAM replaces GPS
RTAB-Map fuses stereo and IMU into a drift-bounded pose.
B
Terrain is scored, not just occupied
Slope, roughness and height variance become real driving cost.
C
Semantics fused into the costmap
YOLO marks mud, water, rock and people; unknown is priced high.
D
Safety supervisor outside the AI
Deterministic code halts on stale sensors or lost pose.
INNOVATION & UNIQUENESS
Deterministic safety, not learned
The stop decision never depends on model confidence.
Camera-first, LiDAR-free terrain
Traversability from vision geometry plus semantics.
Proven by simulation at scale
Randomised Isaac Sim missions score it before hardware.

## Slide 3: TECHNICAL APPROACH
THE VIKINGS
SIH 2025 FINALIST
PROCESSING PIPELINE — camera in, safe velocity out
Stereo Camera + IMU
RGB • depth • inertial
Perception AI
YOLO detect + segment
Visual SLAM
RTAB-Map pose & map
Traversability Costmap
slope • roughness • class
Nav2 Planner
global route
MPPI Controller
local trajectory
Safety Supervisor
veto • slow • stop
Output: /cmd_vel to the UGV base • every block is a ROS 2 node behind a fixed topic and TF contract, so the identical graph runs in simulation and on the real vehicle
LANGUAGES, FRAMEWORKS & TOOLS
Python
perception, tooling
C++
real-time nodes
ROS 2 Jazzy
middleware
Isaac Sim
simulation
PyTorch
model training
OpenCV
vision operations
Docker
reproducible builds
Ubuntu 24.04
target platform
IMPLEMENTATION METHODOLOGY — simulation-first; every phase ships a runnable artefact
PHASE 0
Environment
PHASE 1
Sim navigation
PHASE 2
Visual SLAM
PHASE 3
Terrain layer
PHASE 4
Perception
PHASE 5
Safety logic
PHASE 6
1000+ missions
PHASE 7
Hardware
Design principle: the neural network only answers “what am I looking at?”
Coordinate transforms, mapping, planning, control and the stop decision stay in deterministic, auditable code — so a perception failure degrades into a safe halt, never a collision.

## Slide 4: FEASIBILITY AND VIABILITY
THE VIKINGS
SIH 2025 FINALIST
F
FEASIBLE TODAY
• Nav2, RTAB-Map and elevation_mapping_cupy are mature ROS 2 packages
• Integration and tuning — nothing has to be invented
• Simulation-first: development starts with zero hardware
• Whole loop runs on one RTX workstation (32 GB RAM, 16 GB VRAM)
R
KEY RISKS
• TF, timestamp and calibration errors — the top failure cause
• SLAM drift on featureless or low-texture terrain
• A ditch or water surface misread as drivable ground
• Simulation-to-reality gap in lighting and texture
M
MITIGATION
• Validate the TF tree and clock sync before any AI work
• Stereo + IMU fusion, speed limits, automatic re-localisation
• Unknown terrain is priced expensive, never free
• Domain randomisation over light, texture, noise and obstacles
V
VIABILITY BEYOND SIH
• Identical ROS 2 topic and TF contract, simulation and vehicle
• Only sensor driver and motor interface change on hardware
• Profiles down to a Jetson-class edge computer
• Reusable across BEL surveillance and logistics platforms
ACCEPTANCE GATES — what we will measure, instead of claiming “100% accuracy”
≥ 95%
collision-free randomised missions
< 2%
localisation drift over distance travelled
< 200 ms
emergency-stop software response
≤ 100 ms
perception latency
≥ 20 Hz
control loop rate
≥ 97%
goal completion rate
Every gate is scored automatically from rosbag2 logs against Isaac Sim ground truth, so the numbers are reproducible rather than asserted.

## Slide 5: IMPACT AND BENEFITS
THE VIKINGS
SIH 2025 FINALIST
DRISHTI-UGV
vision-first GPS-denied autonomy
DEFENCE & BEL PLATFORMS
Reconnaissance, patrol and resupply in jammed or GPS-denied terrain.
SEARCH & RESCUE
Entry into collapsed or flooded zones where GPS and comms have failed.
AGRICULTURE & SURVEY
Crop-row navigation and field inspection without RTK base stations.
COST & IMPORT SUBSTITUTION
Cameras replace an expensive LiDAR; the stack is owned in-country.
SAFETY BY DESIGN
A deterministic supervisor halts the vehicle before a failure becomes a collision.
ONE REUSABLE PLATFORM
The same ROS 2 contract retargets to delivery, mining and inspection UGVs.
Measured, not claimed.
Every benefit above is backed by a mission-level number — collision-free completion rate, localisation error against simulator ground truth, path efficiency, recovery rate and emergency-stop latency.

## Slide 6: RESEARCH AND REFERENCES
THE VIKINGS
SIH 2025 FINALIST
NAVIGATION & CONTROL
• ros-navigation / navigation2 — planners, costmaps, behaviour trees
• Nav2 MPPI controller — sampling-based predictive local control
• sacrover / traversability-nav2 — outdoor traversability costmap
VISUAL LOCALISATION & SLAM
• introlab / rtabmap_ros — ROS 2 stereo and RGB-D SLAM with Nav2
• UZ-SLAMLab / ORB_SLAM3 — visual-inertial benchmark (GPLv3)
• LARIAD / Offroad-Nav — closest end-to-end off-road reference
TERRAIN & PERCEPTION
• leggedrobotics / elevation_mapping_cupy — GPU elevation layers
• ultralytics — detection and segmentation models (licence reviewed)
• DepthAnything / Depth-Anything-V2 — monocular depth fallback
SOURCE LINKS & OFFICIAL DOCUMENTATION
› Nav2 framework — github.com/ros-navigation/navigation2
› RTAB-Map ROS 2 — github.com/introlab/rtabmap_ros
› Elevation Mapping CuPy — github.com/leggedrobotics/elevation_mapping_cupy
› Traversability Nav2 — github.com/sacrover/traversability-nav2
› Offroad-Nav reference — github.com/LARIAD/Offroad-Nav
› Isaac Sim ROS 2 bridge — docs.isaacsim.omniverse.nvidia.com
› Isaac Sim workspaces — github.com/isaac-sim/IsaacSim-ros_workspaces
› Ultralytics YOLO — github.com/ultralytics/ultralytics
› Depth Anything V2 — github.com/DepthAnything/Depth-Anything-V2
› Open3D — github.com/isl-org/Open3D
MIT / BSD / Apache-2.0
Nav2, RTAB-Map, elevation_mapping_cupy, Offroad-Nav, Open3D
Licence-reviewed before use
Ultralytics and Depth Anything V2 Small — terms checked
Excluded from the shipped build
ORB-SLAM3 (GPLv3) used only as an offline benchmark
Licence position screened per component before integration; every third-party notice is preserved in the delivered repository.